## Slide 1: Концепция OpenPower и новая стратегия IBM в области HPC Алексей Перевозчиков IBM Server Solutions Product Manager 82189117@ru.ibm.com МГУ, 2 июля 2015г.

## Slide 2: Планы развития процессора POWER
2004
2007
2010
2014
POWER7/7+ 45/32 nm
POWER8 22nm
Eight Cores
On-Chip eDRAM
Power-Optimized Cores
Memory Subsystem ++
SMT++
Reliability +
VSM & VSX
Protection Keys+
POWER6/6+
65/65 nm
Dual Core
High Frequencies
Virtualization +
Memory Subsystem +
Altivec
Instruction Retry
Dynamic Energy Mgmt
SMT +
Protection Keys
POWER5/5+ 130/90 nm
Dual Core
Enhanced Scaling
SMT
Distributed Switch +
Core Parallelism +
FP Performance +
Memory Bandwidth +
Virtualization
More Cores
SMT+++
Reliability ++
FPGA Support
Transactional Memory
PCIe Acceleration
POWER9
Extreme Analytics Optimization
Extreme Big Data Optimization
On-chip accelerators
Notes: 2
2

## Slide 3
Процессор POWER8
Notes: 3
3

## Slide 4: Процессор POWER8
Увеличенные кэши
512 KB SRAM L2 / core
96 MB eDRAM shared L3
Up to 128 MB eDRAM L4 (off-chip)
Память
Up to 230 GB/s sustained bandwidth
Шинные интерфейсы
Durable open memory attach interface
Интегрированный PCIe G3
SMP Interconnect
CAPI (Coherent Accelerator Processor Interface)
Ядра
12 ядер (SMT8)
8 dispatch, 10 issue, 16 exec pipe
2X internal data flows/queues
Enhanced prefetching
64K кэш данных, 32K кэш инструкций
Акселераторы
Криптография
Расширение памяти
Транзакционная память
Поддержка VMM
Перемещение данных / VM
Energy Management
On-chip Power Management Micro-controller
Integrated Per-core VRM
Critical Path Monitors
Технология
22nm SOI, eDRAM, 650mm2, 4.2B transistors

## Slide 5: Ядро POWER8 (относительно POWER7)
VSU
FXU
IFU
DFU
ISU
LSU
2x L1 data cache (64 KB)
2x outstanding data cache misses
4x translation Cache
Wider Load/Store
32B  64B L2 to L1 data bus
2x data cache to execution dataflow
Enhanced Prefetch
Instruction speculation awareness
Data prefetch depth awareness
Adaptive bandwidth awareness
Topology awareness
SMT4  SMT8
8 dispatch
10 issue
16 execution pipes: 2 FXU, 2 LSU, 2 LU, 4 FPU, 2 VMX, 1 Crypto, 1 DFU, 1 CR, 1 BR
Larger Issue queues (4 x 16-entry)
Larger global completion, Load/Store reorder
Improved branch prediction
Improved unaligned storage access

## Slide 6: Memory Buffer Chip …with 16MB Cache…
DDR Interfaces
Scheduler &
Management
16MB
Memory
Cache
Модули памяти наполняются интеллектом
Умная система кэширования
Оптимизация энергии
Надежность
Оптимизированный интерфейс
9.6 GB/s high speed interface
Интеллектуальная надежность
Изоляция сбоев на лету
Уникальная производительность
Уменьшенная латентность fastpath
Cache  latency/bandwidth, partial updates
Логика предсказания
22nm SOI for optimal performance / energy
15 metal levels (latency, bandwidth)
POWER8
Link
Memory Buffer
DRAM Chips
“L4 cache”

## Slide 7: POWER8 Memory Organization (Max Config shown)
POWER8
Memory Buffer
DRAM Chips
16MB
16MB
16MB
16MB
16MB
16MB
16MB
16MB
128 GB
128 GB
128 GB
128 GB
128 GB
128 GB
128 GB
128 GB
Up to 8 high speed channels, each running up to 9.6 Gb/s for up to 230 GB/s sustained
Up to 32 total DDR ports yielding 410 GB/s peak at the DRAM
Up to 1 TB memory capacity per fully configured processor socket

## Slide 8: POWER8 Integrated PCI Gen 3
POWER7
I/O Bridge
GX Bus
PCIe Gen2
PCI Devices
PCIe Gen3
PCI Device
POWER8
Встроенная в кристалл поддержка PCIe Gen 3
Замена GX/Bridge
Минимальная задержка
Gen3 x16 bandwidth (16 Gb/s)

## Slide 9: CAPI (Coherent Accelerator Processor Interface)
Custom
Hardware
Application
POWER8
CAPP
Coherence Bus
PSL
FPGA or ASIC
Специализированные контроллеры
Программные ускорители
POWER8
PCIe Gen 3
Transport for encapsulated messages
Virtual Addressing
Ускоритель работает напрямик с разделяемой памятью
Обмен данными с кэшем процессора.
Исключает накладные расходы ОС и драйверов.
Hardware Managed Cache Coherence
Стандартный механизм блокировок.

## Slide 10
Coherent Accelerator Processor Interface (CAPI) Flow
Flow with a Coherent Model
Shared Mem.
Notify Accelerator
Acceleration
Shared Memory
Completion
DD Call
Copy or Pin
Source Data
MMIO Notify
Accelerator
Acceleration
Poll / Int
Completion
Copy or Unpin
Result Data
Ret. From DD
Completion
Typical I/O Model Flow

## Slide 11: Coherent Accelerator Processor Interface
Non-CAPI
Accelerator
Core
Memory
PCI
CAPI
Accelerator
P8
Core
Memory
PCI
Notes: The coherent accelerator processor interface, or CAPI is a new capability that is part of the POWER8 chip. It allows off-chip accelerators to have coherent access to POWER memory just like traditional power cores. This translates into an easier programming model and significantly less code overhead to accomplish a task.
This slide show a non-CAPI example on the left and a CAPI example on the right. CAPI removes considerable device driver overhead and allows the external accelerator to work with the same memory addresses that the main processors work with. The accelerators can participate in locks just like normal processor threads.
As part of the POWER8 announcement, IBM has made the CAPI interface open to 3rd part developers. This will allow creative designers to develop solutions that IBM has not thought off faster than would be possible by IBM alone.

## Slide 12: CAPI Can Lower Flash Latency
Traditional
PCIe
Drivers
20,000
Instructions
POWER8
CAPI
< 500
Instructions
Traditional
PCIe
CAPI
Device
PCIe Gen3
Electricals
Notes: A significant portion o the realized latency to do an I/O to flash or SSD is the time spent in the processor itself. There is buffer management, LVM overhead, and code spent to manage the pinning and mapping of direct memory access (DMA) devices.
CAPI uses the PCIe physical interface for the easiest programming and fastest, most direct I/O performance
CAPI offers a significant way to reduce that overhead and thereby reduce the latency to do an I/O. The use of CAPI can reduce the I/O instruction path length by 97% going from about 20,000 instructions to less than 500. What could this mean? When combined with FlashSystems it it could:
Attack problem sets otherwise too big for the memory footprint
Deliver fast access to small chunks of data
Achieve high throughput for data or simplify object addressing through memory semantics.

## Slide 13: OpenPOWER Foundation – что, как, зачем.

## Slide 14
Наша миссия - создание открытой экосистемы на базе архитектуры процессора POWER, которая позволит обмениваться знаниями и опытом, инвестировать и разрабатывать продукты, обладающие высокой интеллектуальной ценностью с целью соответствовать потребностям заказчиков и индустрии
Основные особенности OpenPOWER
Это общественная организация, деятельность которой не регулируется кем бы то ни было. Ни коммерческими, ни государственными структурами
Идея близка к концепции ПО с открытым кодом, но в применении к аппаратуре
Отличие от мира СПО – участники консорциума кооперируются, а не конкурируют.
Каждый участник делает свою часть или создаёт свои изделия используя наработки остальных участников сообщества.

## Slide 15
Август 2013 г.
анонс OpenPOWER Foundation.
5 компаний-членов (Google, IBM, Mellanox, NVIDIA, Tyan)
Март 2015 г.
113 членов консорциума
основа-
ние, 2013
Апрель
членов
члена
членов
члена
членов
членов
членов
членов
члена
члена
членов
Май
Июнь
Июль
Август
Сентябрь
Октябрь
Ноябрь
Декабрь
Январь
Февраль
Март
2015

## Slide 16: Члены OpenPOWER
Implementation / HPC / Research
Software
System / Integration
I/O / Storage / Acceleration
Boards / Systems
Chip / SOC

## Slide 17: Начало
Август 2013:
IBM представляет процессор POWER8
Апрель 2014:
Представлены первые прототипы, разработанные участниками консорциума

## Slide 18: Компоненты и системы

## Slide 19: Пример инновационного решения на базе OpenPOWER

## Slide 20: OpenPOWER - опыт Китая
В Январе 2014 компания Suzhou PowerCore и исследовательский институт «Research Institute of Jiangsu Industrial Technology» вступили в консорциум OpenPOWER. В дальнейшем компания Suzhou PowerCore приобрела лицензию на ядро процессора Power8 с целью последующей разработки собственного процессора на его основе.
В течение 2014г. 12 компаний из Китая вступили в OPF (среди которых Inspur и ZTE).
В октябре 2014г. при поддержке министерства промышленности и информационных технологий учрежден альянс «China Power Technology Alliance» с целью ускорения разработки и начала производства собственных ИТ-систем на основе технологий OpenPOWER
На первом симпозиуме OpenPOWER в марте 2015 г. был показан процессор CP1 разработанный Suzhou PowerCore совместно с IBM.
Процессор CP1 будет использоваться провайдером Zoom Netcom в линейке 2-процессорных серверов RedPower к концу 2015 года.
Компании ChuangHe и Inspur намерены в ближайшее время представить собственный дизайн распределённых систем на базе чипа CP1, которые будут выпускаться китайскими брендами, в том числе со встроенной локальной криптографией.

## Slide 22: Состав программной части решений ОЕМ-Партнеров
Сертификация решении (НДВ4 / ФСТЭК): DB2, RHEL, SAP, OC AIX, гипервизор PowerVM
Российские ОС на основе Linux: Заря, МСВС, AstraLinux
Российские /открытые СУБД: PostgreSQL, Ред База Данных

## Slide 23: Несколько слов о стратегии
Notes: ….

## Slide 24: Развитие стратегии аппаратных средств для HPC
Общий дизайн платформы для высокопроизводительных вычислений и высокопроизводительной аналитики
Углубление отношений с технологическими партнёрами
Серверы для данного сегмента в основном 2 сокета
Усиление поддержки InfiniBand и Ethernet
Большая часть производительности на операциях с плавающей точкой будет достигаться за счёт GPU
Стандартные индустриальные стойки и корпуса
  Варианты воздушного и водяного охлаждения

## Slide 25: Стратегия развития процессоров архитектуры POWER
Консолидация усилий и фокус на одном процессоре (чипе) общего назначения для каждого поколения
    Дизайн для более плотной интеграции с вспомогательным оборудованием
    Множественный дизайн модулей обеспечивает различные комбинации памяти и шин I/O
Использование ускорителей подключаемых к процессору для соответствующих платформ и приложений
    FPGA для коммерческих задач, таких как Java, СУБД, аналитика
    GPU для научных и вычислительных задач

## Slide 26: CPU и GPU будут связаны ещё плотнее
Kepler
CUDA 5.5 – 7.0
close
Buffered
Memory
POWER8
PCIe
2014-2015
Pascal
CUDA 8
closer
Pascal
3.0TF
16GB @ 1TB/s
POWER8+
2016
NVLink
SXM2
Volta
CUDA 9
Cache Coherent
POWER9
2017
NVLink 2.0
SXM2
Volta
7.0TF
16GB @ 1.2TB/s
Kepler
1.5TF
12GB @ 288GB/s
PCIe

## Slide 27: Firestone System Concept 2 Socket P8, 2 PCIe GPU System
Power 8 Processor (2x)
190W Sort
Operator Interface
1 USB 3.0
Green, Amber, Blue LED’s
Optional 2x SFF SATA Disk
Disk are tray based for hot swap
Cooling Fans
Counter- Rotating
Hot swap
80mm shown
PCIe slot (1x)
Gen3 PCIe x8 (CAPI)
HHHL Adapter
PCIe slot (2x)
Gen3 PCIe x16 (CAPI)
Gen 3 PCIe x8
HHHL Adapter
NVidia GPU (2x)
Gen 3 PCIe
300W Capable
1 per processor socket
Power Supplies (2x)
1300W
Redundant for commercial, HPC is
non-redundant
Hot Swap
Common Form Factor Supply
Memory DIMM’s Riser (8x)
4 IS DIMMs per Riser
Single Centaur per Riser
32 IS DIMM’s total
IBM CONFIDENTIAL

## Slide 28: Representative large DOE configuration 2015-2018
POWER8 2 Socket Server
2 P8 + 2 Kepler Duo GPU (@2.74 TF/s Boost)
256 GiB SMP Memory (8 GB DDR3 RDIMMs)
48 GiB GPU Memory (HBM stacks)
Compute Rack: 20 Servers/rack
86 TFlop/rack
6.1 TB/rack
32.4 kWatts
System
Cluster Network:
Mellanox IB4X EDR Switch
Compute racks: 26.2PF, 1.86 PB
Storage racks: 72 PB
Management & Gateway racks
10.3 MW
P8:
10 Cores (of 12)
8Threads/core
~ .27 DP TFlop
~ 3.4 GHz
Storage Drawers
Racks | System
Compute | 306
Storage | 32
Scalable system software and data architecture
Technical compilers
Water cooling with RDHX

## Slide 29: Witherspoon System Concept 2 Socket P9, 6 GPU System
Power 9 Processor (2x)
190W Sort
PCIe slot (3x)
Gen4 PCIe
2, x16 HHHL Adapter
1, Shared slot
Working to get a fourth slot
Memory DIMM’s (16x)
8 DDR4 IS DIMMs per socket)
NVidia GPU
2-3 per socket
SXM2 form factor, 300W
NVLink 2.0
Air/Water Cooled
3 per socket always water cooled
Power Supplies (2x)
1900W
Configuration limits for redundancy
Hot Swap
200VAC, 277VAC, 400VDC input
Shown at projected “max” size
Cooling Fans
Counter- Rotating
Hot swap
Thermal analysis to determine size, quanitity
80mm shown
Operator Interface
1 USB 3.0
Green, Amber, Blue LED’s
Optional 2x SFF SATA Disk
Disk are tray based for hot swap

## Slide 30
100+PF System Using P9 & Volta GPU
Compute Rack: 18 Servers/rack
779 TFlop/rack
10.8 TB RAM/rack
14.4 TB Flash
55 kWatts max
System:
100+ Pflops compute 3.7 PB Flash
120 PB Disk
Scalable Active Network:
Mellanox IB4X EDR Switch
Converged 2U server drawer for HPC and Cloud
GSS Rack:
Scalable system software and data architecture
LLVM Open Source compiler
Water cooling
Integrated Local Active Storage
256 Compute Racks
40 Disk Racks
POWER9:
22 Cores
4 Threads/core
0.65 DP TF/s
3.7 GHz
SXM2
Volta:
7.0 DP TF/s
16GB @ 1.2TB/s
POWER9 2 Socket Server
2 P9 + 4/6 Volta GPU (@7 TF/s)
512 GiB SMP Memory (32 GB DDR4 RDIMMs)
64/96GiB GPU Memory (HBM stacks)
Notes: 30
30

## Slide 31: Спасибо за внимание! Вопросы? Алексей Перевозчиков 82189117@ru.ibm.com
Notes: ….

## Slide 32: Storage Class Memory - The Tipping Point for Data-centric Systems
HDD cost advantage continues, 1/10 SCM cost, but
SCM dominates in performance, 10,000x faster than HDD
 | Relative Cost | Relative Latency
DRAM | 100 | 1
SCM | 1 | 10
FLASH | 15 | 1000
HDD | 0.1 | 100000
Source: Chung Lam, IBM
FLASH
(Phase Change)
SCM in 2015
$0.05 per GB
$50K per PB
$0.10 / GB
$0.01 / GB